## Slide 1: Chasing Shadows: Finding Class 1 Sites for Weather Sensors Using Hillshade
Lucas Rosen
GIS 5572

## Slide 2: Overview
Introduction
Setup
Methods and Flowchart
Arc Pro
Earthpy
Results

## Slide 3: Introduction
Weather Stations are useful for many applications in agriculture including finding evapotranspiration and growing degree days
Accuracy of weather stations rely on many factors including Slope, distance from buildings/water, and shading
World Meteorological Organization defines a Class 1 (best) placement for air temperature and humidity sensors as “away from all projected shade when the sun is higher than 5°”
Many urban and photovoltaic studies use hours of sun to get total radiation, but few look at specific altitudes.

## Slide 4: Goal
Use Hillshade Analysis to find Class 1 suitable areas for placement of air temperature and humidity sensors

## Slide 5: Setup: What is needed for a Hillshade
Elevation Data (DSM or DEM)
Zenith (altitude) which is 5°
Azimuth (direction) which varies based on location, date, and time

## Slide 6: Setup: What is needed for a Hillshade
The sun as at 5 degrees twice a day (morning and evening)
Just need to know two dates:
  Winter Solstice
  Summer Solstice

## Slide 7: How to find Azimuth
NOAA’s Sun Calculator was used to find the Azimuth for:
  Winter Solstice Morning : 131.87°
  Winter Solstice Evening: 228.11°
  Summer Solstice Morning: 60.66°
  Summer Solstice Evening: 299.33°

## Slide 8: Data
DSM Data From Data Repository of University of Minnesota
Resolution: 1 meter
Year Collected: 2011
Projection: NAD 1983 UTM 15*

## Slide 9: Flow Chart

## Slide 10: Methods: Arc Pro
DSM was put on the Map and Hillshade was used four times: Once for each date/time

## Slide 11: Methods Arc Pro
Histogram and Arc Pro Documentation Show that shadows are a Hillshade value of 0

## Slide 12: Methods: Arc Pro
Values Greater than 0 were reclassified as 1

## Slide 13: Methods: Arc Pro
All 4 Rasters were multiplied:
    Values of 1 are Class 1 Suitable
    Values of 0 have shadows at some point.

## Slide 14: Methods: Earthpy
Earthpy.Spatial has Hillshade function that works similar to Arc Pro…
But there is a noticeable difference

## Slide 15: Methods: Earthpy
Output looks similar but the values are different (Left: Earthpy Right: Arc Pro)

## Slide 16: Methods: Earthpy
Comparing Histograms shows the values are different (Left: Earthpy Right: Arc Pro)

## Slide 17: Methods: EarthPy
Looking at Earthpy’s source code led to the answer:
Shaded values are between -1 and 1 with anything less than or equal to 0 in shadow
Values + 1 are multiplied by 255 (8-bit) and divided by 2
Plug in 0 for shaded and all shadows are less than or equal to 127.5

## Slide 18: Methods: EartyPy
Once shadows were figured out, Reclassification and Multiplication worked the same way:

## Slide 19: Results
White areas on the map show suitable areas for weather sensors (Left: Earthpy Right Arc Pro)

## Slide 20: Results
Both are similar: slight differences could be due to significant figures used in calculations (Left: Earthpy Right Arc Pro)

## Slide 21: Discussion
Earthpy is needed to do Hillshade on a larger scale because Arc Pro is not supported in MSI
Things to consider (errors):
  Data is from 2011 (needs to be updated)
  Azimuth was determined by the Minnesota Centroid
Place | Lat | Long | Winter AM | Winter PM | Summer AM | Summer PM
Cetroid | 46.39241 | -94.63623 | 131.87 | 228.11 | 60.66 | 299.33
Bottom | 43.452918 | -93.691406 | 129.05 | 230.95 | 61.98 | 298.01
Top | 48.632908 | -93.823242 | 134.44 | 225.57 | 59.48 | 300.52

## Slide 22: Conclusion
Both Arc Pro and Earthpy can use hillshade to produce similar suitability maps
Earthpy could be used with MSI
Need to consider assumptions made in data and analysis